## Slide 1
P2P advanced troubleshooting guide
for ISP and wide network operators

## Slide 2
Introduction
What is this guide?
This is troubleshooting guide to P2P easy connection Dahua protocol.
To whom this guide is written?
This guide is for operators, network experts and engineer who need to troubleshoot Dahua P2P NAT traveral protocol issues on their WAN or on their managed equipements.
To whom this guide is NOT for?
This guide is NOT people who would like to connect a simple installation to P2P.
I am not an network export and I want to make P2P working
Troubleshooting P2P is quite complex, we recommand to use Port address translation as alternative.
P2P advanced troubleshooting

## Slide 3
Types of NAT
P2P advanced troubleshooting

## Slide 4
From: 1.1.1.1:1000 To: 2.2.2.2:2000
Generic principle of Network Address Translation
RFC 3489
Local IP remplaced by External (public) IP
An external random* port is opened
*except for symetric NAT
From: 192.168.1.108:8000 To: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
To: 1.1.1.1:3000 From: 3.3.3.3:3000
NAT Table:
192.168.1.108:8000 -> @:1000
P2P advanced troubleshooting
Types of NAT

## Slide 5
From: 1.1.1.1:1000 To: 2.2.2.2:2000
From: 192.168.1.108:8000 To: 2.2.2.2:2000
Any host can contact the external port
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 3.3.3.3:3000
To: 1.1.1.1:1000 From: 2.2.2.2:3000
To: 192.168.1.108:8000 From: 2.2.2.2:3000
To: 192.168.1.108:8000 From: 3.3.3.3:3000
Full cone NAT
NAT Table:
192.168.1.108:8000 -> @:1000
Types of NAT
P2P advanced troubleshooting

## Slide 6
From: 1.1.1.1:1000 To: 2.2.2.2:2000
From: 192.168.1.108:8000 To: 2.2.2.2:2000
Only the remote host can contact contact back from any of its port
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 3.3.3.3:3000
To: 1.1.1.1:1000 From: 2.2.2.2:3000
To: 192.168.1.108:8000 From: 2.2.2.2:3000
(address) Restricted cone NAT
NAT Table:
192.168.1.108:8000 -> @:1000 (2.2.2.2)
Types of NAT
P2P advanced troubleshooting

## Slide 7
To: 192.168.1.108:8000 From: 2.2.2.2:2000
Port restricted cone NAT
From: 192.168.1.108:8000 To: 2.2.2.2:2000
From: 1.1.1.1:1000 To: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 3.3.3.3:3000
To: 1.1.1.1:1000 From: 2.2.2.2:3000
Only the remote host can contact contact back and from the same port we sent packet
NAT Table:
192.168.1.108:8000 -> @:1000 (2.2.2.2:2000)
Types of NAT
P2P advanced troubleshooting

## Slide 8
To: 1.1.1.1:8000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
From: 1.1.1.1:8000 To: 2.2.2.2:2000
From: 192.168.1.108:8000 To: 2.2.2.2:2000
To: 1.1.1.1:8000 From: 3.3.3.3:3000
To: 1.1.1.1:8000 From: 2.2.2.2:3000
Routeur tries, if possible, to use same source port to expose on internet
Only the remote host can contact contact back and from the same port we sent packet
Symmetric NAT
NAT Table:
192.168.1.108:8000 -> @:8000 (2.2.2.2:2000)
Types of NAT
P2P advanced troubleshooting

## Slide 9
Network topology detection
P2P advanced troubleshooting

## Slide 10
Network type detection
P2P advanced troubleshooting
Network topology detection

## Slide 11
STUN
STUN server provides information from outside (IP address, contacted port, etc.).
STUN server is used to detect local network topology.
P2P advanced troubleshooting
Network topology detection

## Slide 12
TURN
TURN server is the ultimate choice (failback mode) when not option exists to connect two peers together directly.
P2P advanced troubleshooting
Network topology detection

## Slide 13
Troubleshooting steps
1. Identify the topology on both sides of the network
2. Make sure there is no:
Operator NAT (Bouygues)
Host IPv4 sharing (Free)
Symetric NAT (Orange)
Port restricted NAT (Orange)
3. Perform tests from different networks (client device)
4. When possible check routeur NAT table to identify which port and which is not
5. Perform network catpure using a port mirroring and contact Dahua with network capture: julien.blitte@dahuatech.com
P2P advanced troubleshooting

## Slide 14
P2P alternatives
P2P advanced troubleshooting

## Slide 15
To: 192.168.1.108:8000 From: 3.3.3.3:2300
To: 192.168.1.108:8000 From: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 1.1.1.1:1000 From: 3.3.3.3:3000
To: 1.1.1.1:8000 From: 2.2.2.2:2000
Routeur always exposes a defined port and redirect it to same device and port
Any remote hosts that knows the port can access the device. Public IP must be fixed.
This is recommanded solution.
For security reason, external port should always be different than default device port
(Static) Port Address Translation
PAT Table (config):
@:1000 -> 192.168.1.108:8000
NAT Table (dynamic):
...
P2P advanced troubleshooting
P2P Alternatives

## Slide 16
To: 192.168.1.108:1000 From: 2.2.2.2:2000
DMZ
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 1.1.1.1:8000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
To: 1.1.1.1:5000 From: 3.3.3.3:3000
To: 1.1.1.1:4000 From: 2.2.2.2:2000
Routeur forwards all incoming requests to the same device on the network with same destination port
This configuration is a security suicide. All the ports are exposed.
To: 192.168.1.108:4000 From: 2.2.2.2:3000
To: 192.168.1.108:5000 From: 3.3.3.3:3000
Configuration:
DMZ = 192.168.1.108
NAT Table (dynamic):
...
P2P advanced troubleshooting
P2P Alternatives

## Slide 17
To: 1.1.1.1:1000 From: 2.2.2.2:2000
To: 192.168.1.108:8000 From: 2.2.2.2:2000
UPnP: create PAT on port 1000 for 192.168.1.108:8000
UPnP
Device detects router and provide dynamically port to forward. Public IP must be fixed.
This might be at risk (default port exposed, customer unaware)
UPnP Table (dynamic):
@:1000 -> 192.168.1.108:8000
NAT Table (dynamic):
...
P2P advanced troubleshooting
P2P Alternatives